APPLICATION FOR PERMIT

Utility Line Installation

On County R/W

TO THE BOARD OF COUNTY COMMISSIONERS

__________________ COUNTY, STATE OF OKLAHOMA

We (I) the undersigned, hereby petition the Board of County Commissioners of 				 County to grant a permit for the installation of (describe proposed installation)

Give legal description and attach a county map with location clearly marked.

Said line will conform to the following rules:

Petitioners shall notify the Board of County Commissioners 48 hours prior to the actual start of the installation.  There shall also be a 48 hour notification to the Board before any future maintenance or repair work, except in the case of emergency.  In the case of emergency repair notification will be made as soon as possible.  All work by petitioners in the public right-of-way shall be subject to the approval of the Board of County Commissioners, based on the rules listed herein.  Petitioner shall notify the Board upon completion of the installation that a final inspection is required.

When paralleling the roadway it shall be located within 4 feet of the R/W line or the fence line if a fence is in place.  If no fence exists the R/W line shall be located by an Oklahoma registered land surveyor at the petitioner’s expense.  A copy of said survey shall be provided to the Board prior to granting a permit.  In no instance shall a line be placed within the limits of the roadbed.

All underground parallel installations shall be a minimum of 30 inches deep.

All overhead parallel installations shall not cross any point of access to the county road at a height of less than 18 feet.

All underground installations which cross a county road with an asphaltic concrete, oil and chip, or concrete surface shall be jacked.  Cutting of such “hard surfaced” roads will not be permitted.  Crossings of un-surfaced road may be trenched.  When trenching is used, excavated material shall be replaced and compacted to a minimum density of 95% of Standard Proctor maximum density.  Results of the AASHTO T-99 Test as well as results of field density checks shall be submitted to the Board before final acceptance of the installation will be granted.  The Board reserves the right to inspect any and all work during construction.

All underground crossings shall be a minimum of 4 feet below the elevation of the centerline of the road or 30 inches below the elevation of the ditch, whichever is greater.  High pressure gasoline crossings shall be a minimum of 4’ below the elevation of the ditch.

Petitioners agree to assume all responsibility for handling traffic during the construction, repair and maintenance of this line.  Should any lowering, modification or relocation of the line be required during any future reconstruction or maintenance of the road, said lowering, modification or relocation shall be made without claim against the County.  Should any damage to the line occur in the regular operation of the road work, said damage shall be repaired by the petitioners or their successors, without claim against the County.

Petitioner agrees to hold the County blameless for any damage to persons or property caused by the construction, maintenance operations or repair of its facilities, on, over, or under said right-of-way, and agrees to reimburse the County for any and all monies expended by it in repairing any damage to the road caused by the construction, maintenance and operations of the petitioners.

Failure on the part of the petitioner to comply fully with the rules herein stated shall cause the petitioner to forfeit his right to easement on said County R/W, as per O.S. 69§1401 1981.

(Approval Certificate

on reverse side)		Company Name				Company Representative

Company Address			Phone #

Emergency (24 hr) #

Adopted and passed this the 	 day of 			, 2010.

BOARD OF COUNTY COMMISSIONERS

COUNTY, OKLAHOMA

Chairman

ATTEST:

Member

County Clerk					Member

| R-__-__ |  |
| --- | --- |
| 6 | 5 | 4 | 3 | 2 | 1 | T-__-__ |
| 7 | 8 | 9 | 10 | 11 | 12 |  |
| 18 | 17 | 16 | 15 | 14 | 13 |  |
| 19 | 20 | 21 | 22 | 23 | 24 |  |
| 30 | 29 | 28 | 27 | 26 | 25 |  |
| 31 | 32 | 33 | 34 | 35 | 36 |  |